The GrADS map background file has the following format:

      3 byte header.  This header always starts the file,
      and always preceed each data record.  The first
      byte of the header determines the record type.
      When the value is 1, it is a data record, consisting
      of some number of lat/lon points.  If the value is 2,
      it is a "skip" record, allowing some large part of the
      map file to be skipped over if appropriate (for efficiency
      reasons).

      Record type 1:

          Byte 0:  1
          Byte 1:  Indicates the type of this record.
          Byte 2:  Count of the number of points in this record,
                   each point consisting of six bytes,
                   being a pair of values 3 bytes each.
          Bytes 3 to n:  This consists of pairs of values,
                   six bytes per pair.  Each pair is lon,lat,
                   three bytes each.

     General Notes:

          1)  Byte ordering is always "normal".  In other
              words, for a three byte value, the high order
              byte is encountered first in the byte stream,
              and the low order byte is encountered last.
          2)  Map point pairs are always three bytes for
              longitude, followed by three bytes for latitude.
          3)  The integer 3 byte values are converted to
              real world values by:
                 lon = float(p1)/1e4
                 lat = float(p2)/1e4 - 90.0
          4)  Longitude values are always between 0 and 360;
              Latitude values are always between -90 and 90.

      Notes on Record type 1:

          1)  The record type (valued 0 to 255) is used to
              differentiate between line types
              such as coastlines, roads, rivers, etc.
              The user has control over whether certain
              type values are plotted and how they are plotted.
          2)  By default, type 0 is always plotted, and types
              1 and 2 are plotted when 'set poli on' is
              used, and types 1 and 2 are not plotted when
              the user issues 'set poli off'.  This is provided
              for upward compatability with past map versions.
          3)  The map backgrounds provided with GrADS have
              coastlines as type 0, country boundaries as
              type 1, and state/provence boundaries as type 2.
          4)  All the points in the record are considered to be
              one line, with all the points connected via a
              "pen-down" motion.
          5)  Each line is considered to start with a "pen-up"
              move to the start of the line.
          6)  Lines consisting of more than 255 points must be
              split before being written to the file.

      Record type 2:

          Byte 0:  2
          Byte 1:  Start Type
          Byte 2:  End Type
          Bytes 3 to 6:  File position (4 bytes long).
          Bytes 7 to 18:  Two point pairs, indicating a lat-lon range.

      Notes on record type 2:

          1)  Record type 2 is a "skip" record.  A skip record
              can be used to skip over parts of the file that
              are not relevent to the current display.
              Optionally, when reading the file, you can ignore
              the skip record and just read past it.  And it is
              not required that skip records be used when creating
              a map file.
          2)  The skip record describes a range of map types
              (start-type to end-type) and a range of lat-lon
              values (lon1,lat1 to lon2,lat2).  These ranges
              describe what map regions and line types are
              contained next in the map file.  If the current
              display does not include anything in this range,
              then the described portion of the file may safely
              be skipped.
          3)  The file position (bytes 3 to 6) contain the byte
              location in the file to start reading at, should
              a skip be desirable.
          4)  A skip-to file location of zero indicates the
              skip would take you to end-of-file.
          5)  Setting up a skip sequence in your map file may
              be fairly complicated, since it usually requires
              segmenting the data into regions on the globe or
              putting all line types together in the file, or
              both.  This usually implies writing the file
              using several passes, so that the skip-to location
              can be inserted on the last pass.
          6)  An example of the use of skip records is the hires
              data set provided with GrADS.  This data set is
              segmented into four global regions, and line type
              zero is followed by line type 1 which is followed by
              line type 2.  The sequence of records is:

        ---------- - skip record for line type 0, skipping to
        |            the start of line type 1.
        |
        |    ----- - skip record for lon range 0 to 180 and
        |    |       lat range -90 to 90.
        |    |
        |    |  -- - skip record for lon range 0 to 180 and
        |    |  |    lat range -90 to 0.
        |    |  |
        |    |  |    -  data records for line type 0, lon range
        |    |  |       0 to 180, lat range -90 to 0.
        |    |  --->
        |    |  ---- skip record for lon range 0 to 180 and
        |    |  |    lat range 0 to 90
        |    |  |
        |    |  |    - data for lon range 0 to 180, lat range
        |    |  |      0 to 90.
        |    ------>
        |
        |    ------- skip record for lon range 180 to 360 and
        |    |       lat range -90 to 90
        |    |
        |    |  ---- skip record for lon range 180 to 360 and
        |    |  |    lat range -90 to 0
        |    |  |
        |    |  |    - data for lon range 180 to 360, lat
        |    |  |      range -90 to 0
        |    |  --->
       \|/  \|/  ....etc....


          7)  The programs that created and read the GrADS
              map backgrounds are available as examples.